## Slide 1
Encoders
Pots
Oran’s fancy chip
Motors
FPGA
RTOS
MLC
UDP
Serial
HES
Teensy
I2C
C#
LabVIEW
LabVIEW
C
C++
UDP

## Slide 2: Control Box Connections

## Slide 3
A
Motor 1 Dir
Motor 1 PWM
Motor 1 en/dis
B
14.12.10
Reserved for Serial
Oran’s chip
Motor 2 Dir
Motor 2 PWM
Motor 2 en/dis

## Slide 4
GND
ADIO1
BDIO1
+5V
+24V
Motor 2 Vout
Motor 1 Vout

## Slide 5
+24V
external
GND
external
myRIO GND
A
B
+5V myRIO
Motor 1 A
Motor 1 B
Motor 2 A
Motor 2 B
1
2

## Slide 6: Oran’s Board
Ping/Pong – Send ‘s’ and receive encoder values
Unable to do Serial via FPGA, so this will be VISA on RT only.
Baud rate = 115200

## Slide 7: FPGA
Old Responsibilities:
Obtain Pots, Read encoders
FK
Data to RT = pot readings, theta readings, current xy.
Obtain motor directions, enable/disable, gains
Create PWM
Data to motors = PWM, enable, directions
New Responsibilities:
Obtain motor directions, enable/disable, gains
Create PWM
Data to motors = PWM, enable, directions

## Slide 8: Obtaining data from Oran’s Chip 1.
Initialise Serial communication.
Baud rate is 115200
MyRIO serial comms port is connector B

## Slide 9: Obtaining data from Oran’s Chip 2.
Write ‘s’ to serial to request data from Oran’s fancy chip
Read all the bytes at the port (there will be 16 bytes)

## Slide 10: Obtaining data from Oran’s Chip 3.
When reading the buffer, nonsense characters are received.
Convert these to an unsigned byte array.
The data is in the format:
Enc 0 pos
Enc 1 pos
Enc 0 vel
Enc 1 vel

## Slide 11: Obtaining data from Oran’s Chip 4.
The session must be closed at the end

## Slide 12: Decoding data from Oran’s Chip 1.
Enc 0 pos
Enc 1 pos
Enc 0 vel
Enc 1 vel
Currently only care about position since the velocities are not working well, so only the first 8 bytes of data are used.
The C++ code for decoding:

## Slide 13: Decoding data from Oran’s Chip 2.
Decoding encoder 0
Byte 0
Byte 1
Byte 2
Byte 3

## Slide 14: Decoding data from Oran’s Chip 3.
Decoding encoder 1
Byte 4
Byte 5
Byte 6
Byte 7

## Slide 15: Decoding data from Oran’s Chip 4.
Thus, we have the counts in each encoder. It is necessary to turn the counts into an angle (rad)
The encoder has 1024 pulses per revolution, or 4096 counts per revolution (because its quadrature)
Shoulder
Elbow
motor
motor
Gearbox
Spur1
15:1
Spur2
8:3
Gearbox
Bevel1
2:1
Bevel2
35:1
40 motor turns = 1 rev = 163840 counts
70 motor turns = 1 rev = 286720 counts

## Slide 16: Decoding data from Oran’s Chip 5.
Shoulder
Elbow
40 motor turns = 1 rev = 163840 counts
1 count = 360/163840 = 0.00219726562 deg = 2π/163840 = 3.83495196097794e-5 rad
70 motor turns = 1 rev = 286720 counts
1 count = 360/286720 = 0.00125558035714285714285714285714 deg = 2π/286720 = 2.191401125545480038e-5 rad

## Slide 17: Teensy 3.2 to myRIO
Force Sensor I2C Documentation

## Slide 18: Teensy Connection
Vin (+5V)
GND
+3.3V (Vout)
AI0
AI1
AI2
AI3
SDA
SCL

## Slide 19: myRIO Connection
+5V (Vout)
SDA
SCL
GND

## Slide 20: All Connections.
MyRIO
+5V Vout
SCL
SDA
GND
Teensy
+5V Vin
SCL
SDA
GND
+3.3V Vout
AI0
AI1
AI2
AI3
All HES
GND
+3.3V Vin
HES 1 Vout
HES 2 Vout
HES 3 Vout
HES 4 Vout

## Slide 21: Teensy code – Initialisation
#include <Wire.h>
int a = 0; // HES 1 raw voltage reading
int b = 0; // HES 2 raw voltage reading
int c = 0; // HES 3 raw voltage reading
int d = 0; // HES 4 raw voltage reading
volatile byte dataPacket[8]; // array of bytes to send
volatile byte ha = 0; // High byte for HES1
volatile byte la = 10; // low byte for HES1
volatile byte hb = 0; // High byte for HES2
volatile byte lb = 0; // low byte for HES2
volatile byte hc = 11; // High byte for HES3
volatile byte lc = 0; // low byte for HES3
volatile byte hd = 0; // High byte for HES4
volatile byte ld = 13; // low byte for HES4
bytes and byte array declared as volatile, since it is
necessary to inform the compiler that the values may
change via interrupts, so that the compiler
doesn't optimise the code away.

## Slide 22: Teensy code – setup function
void setup() {
Wire.begin(1); // join i2c bus with address #1
Wire.onRequest(requestEvent); // register event
}
The event is processed as an interrupt, which is why the bytes were
Declared as volatile.

## Slide 23: Teensy code – main loop function
void loop() {
a = analogRead(0); //read raw bits for HES 1
b = analogRead(1); //read raw bits for HES 2
c = analogRead(2); //read raw bits for HES 3
d = analogRead(3); //read raw bits for HES 4
getByte(); // cast to high and low bytes
fillArray(); // build byte array for transfer
delay(1);
}
These 2 functions build the array ready for transfer

## Slide 24: Teensy code – getByte() function
void getByte() {
ha = highByte(a);
la = lowByte(a);
hb = highByte(b);
lb = lowByte(b);
hc = highByte(c);
lc = lowByte(c);
hd = highByte(d);
ld = lowByte(d);
}
This function casts the data for each sensor into a high byte, and a low
Byte. This is necessary because the data is greater than 255, or longer than 1 byte
0000001000110110
Eg, 566 dec = 0000001000110110 bin
00000010
00110110
High byte
low byte

## Slide 25: Teensy code – fillArray() function
void fillArray() {
dataPacket[0] = ha;
dataPacket[1] = la;
dataPacket[2] = hb;
dataPacket[3] = lb;
dataPacket[4] = hc;
dataPacket[5] = lc;
dataPacket[6] = hd;
dataPacket[7] = ld;
}
This function builds the 8-byte array
00000010
00110110
High byte a
low byte a
00000010
00110110
High byte b
low byte b
00000010
00110110
High byte c
low byte c
00000010
00110110
High byte b
low byte d

## Slide 26: Teensy code – I2C Event function
void requestEvent() {
Wire.write((byte*)dataPacket, 8);
}
This function fires when the myRIO (I2C Master) sends a request
For data.
The array of 8 bytes (the data packet) is written to the data line

## Slide 27: myRIO code

## Slide 28: Training the Force Neural Network 1
Can be found in trainNet.m in PhD MATLAB folder.
Init Phase:
clc; % Clear the command window
clear; % Clear the workspace
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%%%%%%%%%%%%%%%%%%%%%% Get data and process %%%%%%%%%%%%%%%%%%%%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%import testdata
sizedata = size(csvread('testdata.csv',1,0));
rawdata = csvread('testdata.csv',1,0,[1,0,sizedata(1),5]);
%randomise row order to limit the risk of local minima
data = rawdata(randperm(size(rawdata, 1)), :);
% data is in the format: force, orientation, raw1, raw2, raw3, raw4

## Slide 29: Training the Force Neural Network 2
Can be found in trainNet.m in PhD MATLAB folder.
%Create training vectors
raw1 = data(:,3)/1000; %Raw bits from sensor 1
raw2 = data(:,4)/1000; %Raw bits from sensor 2
raw3 = data(:,5)/1000; %Raw bits from sensor 3
raw4 = data(:,6)/1000; %Raw bits from sensor 4
%Create answer vectors
Fx = (data(:,1).*cos((deg2rad(data(:,2)))));
%Process data to remove any tiny numbers (such as xE-17)caused by trig
c=0;
for count = 1:sizedata(1)
c=c+1;
if Fx(c) <0.01 && Fx(c) > -0.01
Fx(c) = 0;
end
end
Pre-processing, to ensure inputs are between
0 and 1 necessary for neural network training

## Slide 30: Training the Force Neural Network 3
Can be found in trainNet.m in PhD MATLAB folder.
%Scale to work nicely with NN maths
Fx = Fx/100;
Fy = (data(:,1).*sin((deg2rad(data(:,2)))));
%Process data to remove any tiny numbers (such as xE-17)caused by trig
c=0;
for count = 1:sizedata(1)
c=c+1;
if Fy(c) <0.01 && Fy(c) > -0.01
Fy(c) = 0;
end
end
%Scale to work nicely with NN maths
Fy = Fy/100;

## Slide 31: Training the Force Neural Network 4
Can be found in trainNet.m in PhD MATLAB folder.
Training Phase:
% Solve an Input-Output Fitting problem with a Neural Network
% Script generated by Neural Fitting app
x = [raw1'
raw2'
raw3'
raw4'];
t = [Fx'
Fy'];
Network inputs
Network Answers

## Slide 32: Training the Force Neural Network 5
Can be found in trainNet.m in PhD MATLAB folder.
% Choose a Training Function
% For a list of all training functions type: help nntrain
% 'trainlm' is usually fastest.
% 'trainbr' takes longer but may be better for challenging problems.
% 'trainscg' uses less memory. Suitable in low memory situations.
trainFcn = 'trainlm'; % Levenberg-Marquardt backpropagation.
% Create a Fitting Network
hiddenLayerSize = [20,10];
net = fitnet(hiddenLayerSize,trainFcn);
Select back-propagation technique
Create the network, define size and
Training function

## Slide 33: Training the Force Neural Network 6
Can be found in trainNet.m in PhD MATLAB folder.
% Choose Input and Output Pre/Post-Processing Functions
% For a list of all processing functions type: help nnprocess
net.input.processFcns = {};
net.output.processFcns = {};
Note: I have defined the pre and post processing functions as empty, since I have done my own
Pre and post processing to make the translation to LabVIEW code easier.

## Slide 34: Training the Force Neural Network 7
Can be found in trainNet.m in PhD MATLAB folder.
% Setup Division of Data for Training, Validation, Testing
% For a list of all data division functions type: help nndivision
net.divideFcn = 'dividerand'; % Divide data randomly
net.divideMode = 'sample'; % Divide up every sample
net.divideParam.trainRatio = 70/100;
net.divideParam.valRatio = 15/100;
net.divideParam.testRatio = 15/100;
Divide the training data into a training set, a validation set and a test set.

## Slide 35: Training the Force Neural Network 8
Can be found in trainNet.m in PhD MATLAB folder.
%Set a training goal
net.trainParam.goal= 1e-6;
net.trainParam.epochs=15000;
net.layers{1}.transferFcn = 'tansig';
net.layers{2}.transferFcn = 'tansig';
net.layers{3}.transferFcn = 'tansig';
15000 epochs, training goal is an error of 1e-6.
Activation function in hidden layers and output layer
Is the sigmoid function.
Sigmoid function as handcoded in MATLAB
Sigmoid function in labVIEW
Can be found in function threshold.m in PhD MATLAB folder.

## Slide 36: Training the Force Neural Network 9
Can be found in trainNet.m in PhD MATLAB folder.
% Choose a Performance Function
% For a list of all performance functions type: help nnperformance
net.performFcn = 'mse'; % Mean Squared Error
% Train the Network
[net,tr] = train(net,x,t);
% Test the Network
y = net(x);
e = gsubtract(t,y);
performance = perform(net,t,y)
Train the network
Test the network

## Slide 37: Training the Force Neural Network 10
Can be found in trainNet.m in PhD MATLAB folder.
% Generate a matrix-only MATLAB function for neural network code
% generation with MATLAB Coder tools.
genFunction(net,'myNeuralNetworkFunction','MatrixOnly','yes');
y = myNeuralNetworkFunction(x);
Export the network as matrices
Trained network can be found in myNeuralNetworkFunction.m in PhD MATLAB folder.

## Slide 38: Old Code for refactoring

## Slide 39: Old myRIO code 1
Current architecture.
1.
2.
3.
4.

## Slide 40: Old myRIO code 2
This is an FGV that holds a ‘Shut down’ user event.
There is a parallel loop for every main VI in section 3
which monitors this user event, waiting to shutdown the system.
I will keep this, its important for safety.

## Slide 41: Old myRIO code 3
These obtain references to notifiers and queues. All notifiers and queues are in FGVs. A good system which I
Will keep, but some of these are no longer relevant since they pertain to legacy code, such as TCP comms

## Slide 42: Refactoring the myRIO code 4
Row 1 controls the controller – will need to keep in some form
Row 2 controls the logging – Will Need to keep in some form
Row 3 is the low level controller - will need to keep in some form
Row 4 controls the game communication (TCP) – Now UDP with MLC
Row 5 controls the host communication. – Legacy, no longer Req
Row 6 controls the error handling. - will need to keep in some form

## Slide 43: New Refactored Code

## Slide 44
Very Similar
Main Architecture
Note that queues are not
Destroyed until all module
Loops have completed

## Slide 45
1. Program Control Module: Starts and stops all other modules
2. External Communications module: Controls UDP connection up to the MLC
And a separate UDP connection from MLC
3. DAQ Module: Performs Hardware DAQ. Currently Serial to Oran’s
Chip and i2C to my Teensy
4. Low Level Control Module: Performs the specified control type, sends motor
Demand info to FPGA
5. Logs system info, such as errors and starts etc
6. Handles Errors.

## Slide 46
Create a shutdown event, which closes all loops when a stop button is pressed on
The RT front panel.

## Slide 47
Create a Shutdown User Events Functional
Global Variable.

## Slide 48
Shutdown user event fires, Shutdown is set to true,
Which forces the shutdown state for every parallel
Loop (of which there are many in each library)
These structures are in each of the module
Main VIs.

## Slide 49
The next series of slides documents the queue design and initialisation

## Slide 50
Each Module is controlled by a library. The intermodule communication occurs
With queues and notifiers, which are initialised here.
1.
2.
3.
4.
5.
6.
Each Module has a queue, whereby all modules (including the module in question)
may enqueue a message to a particular module.
i.e. All modules may send a message to the logging module using the logging module
Queue.

## Slide 51
Queues 1.

## Slide 52
Queues 2.

## Slide 53
Queues 3.

## Slide 54
Queues 4.

## Slide 55
Queues 5.

## Slide 56
Queues 6.

## Slide 57: Starting procedure
This series of slides documents the start up procedure from turning on up until the normal running of the system.

## Slide 58: Starting procedure 1.
Shutdown User Event FGV is created

## Slide 59: Starting procedure 2.
Queues are created

## Slide 60: Starting procedure 3.
All Modules run simultaneously

## Slide 61: Starting procedure 4.
Program Control Module Init Phase 1: Send ‘Start’ Notifier

## Slide 62: Starting procedure 5.
Program Control Module Init Phase 2: Enqueue Successful Module Start Log:

## Slide 63: Starting procedure 6.
Program Control Module Init Phase 3: Enqueue Start Notifier Sent Log and initialise variables:

## Slide 64: Starting procedure 7.
External Communication Module Init Phase 1: Do nothing until start notification received

## Slide 65: Starting procedure 8.
External Communication Module Init Phase 2: Send successful module start log:

## Slide 66: Starting procedure 9.
External Communication Module Init Phase 3: init UDP Connections:

## Slide 67: Starting procedure 10.
Data Acquisition Module Init Phase 1: Do nothing until start notification received

## Slide 68: Starting procedure 11.
Data Acquisition Module Init Phase 2: Set up DAQ internal producer/consumer queues
There is 1 queue for the Encoder data, and a separate
Queue for the force data.

## Slide 69: Starting procedure 12.
Data Acquisition Module Init Phase 3: Send successful encoder acquisition loop start log.

## Slide 70: Starting procedure 13.
Data Acquisition Module Init Phase 4: initialise serial communications with Oran’s chip

## Slide 71: Starting procedure 14.
Data Acquisition Module Init Phase 5: Send successful force acquisition loop start log.

## Slide 72: Starting procedure 15.
Low Level Control Module Init Phase 1: Open Connection to FPGA Top Level VI

## Slide 73: Starting procedure 16.
Low Level Control Module Init Phase 2: Send successful module start log:

## Slide 74: Starting procedure 17.
logging Module Init Phase 1: Do nothing until start notification received

## Slide 75: Starting procedure 18.
logging Module Init Phase 2: Open Log streaming file:
The log file can be accessed on the MyRIO:
Open internet explorer
Type in the IP Address 172.22.11.2/files
Username is admin. Password is blank
Log can be found in /home/lvuser

## Slide 76: Starting procedure 19.
logging Module Init Phase 3: Send successful module start log:

## Slide 77: Starting procedure 20.
Error Module Init Phase 1: Do nothing until start notification received

## Slide 78: Starting procedure 21.
Error Module Init Phase 2: Send successful module start log:

## Slide 79: Normal Running 1
Each module runs
Simultaneously.

## Slide 80: Normal Running 2: Program Control Module
Dequeue a message for handling. The message is passed
Into a case structure for handling.
Messages currently include:
Error.
Shutdown.

## Slide 81: Normal Running 3: Program Control Module
Very similarly, if there is an error, generate
‘shutdown’ User Event.
If there is a ‘Shutdown’ message from
MLC, generate
‘shutdown’ User Event.

## Slide 82: Normal Running 4: External Comms Module
Data is transferred by UDP:
MyRIO
MyRIO, IP: 172.22.11.2
PC, IP: 172.22.11.1
Sending Port: 60000
Sending Port: Unknown
Listening Port: 60006
Listening Port: 65530

## Slide 83: Normal Running 5: External Comms Module
Read the outbound data from the FGV
Convert the cluster to a JSON packet
Write the data to the outbound UDP connection

## Slide 84: Normal Running 6: Get Data Out VI
Read all the Data from the Data FGV. Unbundle only the outbound data.

## Slide 85: Normal Running 7: Get Data Out VI
Outbound data:

## Slide 86: Normal Running 8: to JSON VI
Convert the cluster to a JSON string for transfer through UDP

## Slide 87: Normal Running 9: Transmit UDP VI
Transmit the outbound
Data from the myRIO
To the PC.

## Slide 88: Normal Running 10: External Comms Module
Read the inbound data from the UDP connection
Convert the JSON String to a cluster
Write the data to the FGV
Inform CTRL module of shutdown if true
1.
2.
3.
4.

## Slide 89: Normal Running 11: UDP Listen VI
1.
2.
3.

## Slide 90: Normal Running 12: UDP Listen VI 1
Attempt to read from the UDP connection.
3 potential outcomes:
Successful data read
Timeout error 56
Other error

## Slide 91: Normal Running 13: UDP Listen VI 2
No Error, successful data read. Write the data to an FGV
Error 56, timeout. Do not write any data. Clear the error.
Other Error. Do not write any data. Do not clear the error.

## Slide 92: Normal Running 14: UDP Listen VI 3
Read the data from the FGV and pass it out.
This means that the last piece of successfully acquired data
Is the data which will be used by the rest of the program.

## Slide 93: Normal Running 15: from JSON VI
Convert the raw JSON string into
A cluster of input data.

## Slide 94: Normal Running 16: Set Data in VI
Write data in to all data FGV

## Slide 95: Normal Running 17: Set Data in VI
Data from the MLC to the myRIO:

## Slide 96: Normal Running 18: External Comms Module
Check for errors. This VI is used in every loop in every module.
If any errors occur, inform the Error Handling module and then
Clear the error to prevent infinite error loops.
1.
Error Here
2.
Error Here. Pass error
To Error Handling Module
3.
Error has been cleared.
No error here.

## Slide 97: Normal Running 19: Error Handler VI
Inputs: Source Module of the Error
Error
Outputs: No Error (error is cleared)

## Slide 98: Normal Running 20: Error Handler VI

## Slide 99: Normal Running 21: DAQ Module
This module consists of 2 producers and 2 consumers.
Module internal queues handle data transfer between them

## Slide 100: Normal Running 22: DAQ Module encoder producer
1.
2.
3.
4.
Write ‘s’ to serial. When the
Chip receives this it puts data on the line
2. Read all 16 bytes of data from the serial
Line.
Enqueue the unprocessed data onto the
Producer/consumer encoder queue.
Check status of stop button to decide
Which state is next.

## Slide 101: Normal Running 23: DAQ Module force producer
1.
2.
3.
Write an empty byte to the teensy via
I2C, to prompt the teensy to put a data packet
onto the bus
2. Enqueue the unprocessed data onto the
Producer/consumer force queue.
3. Check status of stop button to decide
Which state is next.

## Slide 102: Normal Running 24: DAQ Module Encoder consumer
1.
2.
3.
Convert the serial string to an unsigned byte array,
Rebuild the bytes into encoder counts
2. Convert the encoder counts to an angle in Radians
3. Perform the forward kinematics

## Slide 103: Normal Running 25: Scale encoder VI.
As per slides 14 and 15.

## Slide 104: Normal Running 26: counts to angle VI.
As per slides 16 and 17

## Slide 105: Normal Running 27: forward kinematics

## Slide 106: Normal Running 28: forward kinematics 2
Note that the y offset in the above
Slide moves the origin.

## Slide 107: Normal Running 29: DAQ Module force consumer
1.
2.
Recombine the bytes to obtain the raw
Voltage readings from the teensy
Run the raw bits through the Neural Network
To obtain Fx and Fy.

## Slide 108: Normal Running 30: Build bits VI
Uses the ‘join numbers’ function
To rebuild the raw voltage readings

## Slide 109: Normal Running 31: neural network VI
2.
1.
3.
4.
5.
Pre-processing – inputs to the network must range from 0-1,
thus divide by 1000
Hidden layer 1.
Hidden layer 2.
Output layer.
Post-processing – Newtons from -100 to 100.

## Slide 110: Normal Running 32: Low Level Control Module
1.
2.
3.
4.
5.
Read data from ‘All Data’ FGV
Low Level Control VI, generate
Motor demands according to control
Scheme.
3. Enable motors VI, generate a Boolean
For each motor.
4. Write motor information to FPGA
5. Check status of stop button to decide
Which state is next.

## Slide 111: Normal Running 33: Enable Motors VI
A motor is enabled when the demand
Is not 0, no matter what direction (i.e.
+ve or –ve)

## Slide 112: Normal Running 34: Logging Module
1.
2.
3.
4.
5.
1. Get a message from the queue
2. Format the message correctly
3. Set the log to write at the end
Of the file.
4. Write the log
5. Check status of stop button to decide
Which state is next.

## Slide 113: Normal Running 35: Format log VI
Require the log to be in the following format:
Timestamp
Calling Module
1.
Message
Error Number
Error Source
Timestamp
Calling Module
2.
Message
Error Number
Error Source
Timestamp
Calling Module
3.
Message
Error Number
Error Source
Timestamp
Calling Module
4.
Message
Error Number
Error Source
Timestamp
Calling Module
5.
Message
Error Number
Error Source

## Slide 114: Normal Running 36: Format log VI
1.
1: unbundle message, 2: Parse error (if error exists), 3: Format log into string
2.
3.

## Slide 115: Normal Running 37: Error Handling Module
Receive Error Message
Log Error and Source
Inform Program Control Module of Error
Determine next state.
1.
4.
2.
3.

## Slide 116: Normal Running 38: Send Error Log VI
Enqueue error log at front
Of log queue

## Slide 117: Normal Running 39: Send Error Log VI
Inform program
Control module
That an error has
Occurred.
Error location
“Error”

## Slide 118: Normal Running 40: Common Errors
DAQ Module: I2C Error -363011. This error occurs when the I2C comms has failed. During testing,
this typically occurs when the SCL or SDA lines are switched, or one of them is disconnected. If the
cable is reconnected whilst code is running, the error typically disappears.
DAQ Module: Serial Error/warning 1073676294. This error occurs when the serial comms has failed. During testing,
this typically occurs when the lines aren’t physically connected. During testing it has become apparent that this warning
Almost always is present, even when things are working well.
External Comms Module: UDP Read Timeout Error 56. This error occurs trying to read UDP data when there
is none on the wire. This error is handled internally in the external comms module, and should never be noticed
by the user.

## Slide 119: FPGA
The FPGA is responsible only for controlling the motors. It does not perform any DAQ.
INPUTS: Motor demand, motor direction, motor enable/disable
OUTPUTS: Motor enable/disable, Motor direction, Motor PWM

## Slide 120: FPGA 1
INPUTS

## Slide 121: FPGA 2
Initialisation:
Set demands to 0 and disable motors to
Ensure that the robot does not move upon
Startup.
There is a dataflow dependency on the Boolean
Which ensures that no other FPGA code runs
Until the initialisation is complete.

## Slide 122: FPGA 3
Connected as per slide 3 of this document

## Slide 123: FPGA 4
This loop calculates the Duty Cycle from the demand, and also sets the motor direction

## Slide 124: FPGA 5
This loop writes the PWM to the motor control boards

## Slide 125: Admittance Control Library
This library is used within the LowLevelControl Module.
Inputs: PID Gains, Admittance Gains, All Data/
Outputs: Motor 1 direction and demand (0-100), Motor 2 direction and demand (0-100)

## Slide 126: Admittance Control Library 2
1st action is to check whether assistance is enabled.
If enabled, move to control as normal.
If disabled, no control will be performed.

## Slide 127: Admittance Control Library 3
With Assistance enabled, the first action
Is to extract the necessary control data from the
‘All Data’ FGV

## Slide 128: Admittance Control Library 4
2.
1.
2 actions then occur in parallel.
It is determined if there is a new target
(and also if the game or the controller is
In charge of trajectory generation).
2. It is determined whether the target has been met.

## Slide 129: Admittance Control Library 5
If the xposition = xtarget (within deadzone)
If the yposition = ytarget (within deadzone)
AND
The program outputs a ‘1’, which is used to
Turn off control further along.

## Slide 130: Admittance Control Library 6
Determines if the target is new or not. If a new target, a Boolean is output
To the PID further along to reset Integral.
Determines if the target is new or not. If a new target, a Boolean is output
To the PID further along to reset Integral and also Min Jerk Parameters are reset.
Then, next position is calculated by min jerk trajectory.

## Slide 131: Admittance Control Library 7
1.
2.
3.
1. Determine if new target.
2. Set initial conditions for new min jerk trajectory if new target.
3. Reset FGV timer for min jerk trajectory if new target.

## Slide 132: Admittance Control Library 7
Calculate the next point on the minimum jerk trajectory according to the equation

## Slide 133: Admittance Control Library 8
If target met, generate no motor demands
If target not met, generate motor demands

## Slide 134: Admittance Control Library 8
2.
1.
3.
Forces go through admittance filter
Inverse kinematics derive next desired
Point.
3. Position PID generates motor demands

## Slide 135: Admittance Control Library 9
Apply admittance filter as per equation derived.

## Slide 136: Admittance Control Library 10
CHECK OUTPUT IN RADDDDDD. NEED OUTPUT IN RAD!!!!!!!!!!!!!!!!!!!!!!!!!!!!

## Slide 137: Admittance Control Library 11
1.
2.
3.
4.
1. All angles in radians
2. PID control. Integral is reset when new target
3. Convert -100 – 100 to 0-100 and direction
4. Output demand 0-100 and directions